- Content
  - Theory, introduction, Normalising Flows, MAF
  - Evaluate two abilities of Normalising Flows, density estimation and sampling:
    - How close it gets to learned distributions
    - Sample quality, real world dataset
- Density Estimation
  - 1D example
  - black: density function
    - do not have that, want that
  - blue plusses: samples from this distribution
    - have that, datasets
  - Motivation
    - Bayes
    - Anomaly Analysis
  - Histogram
    - 20 bins
    - counts samples that fall in a bins range
    - normalises
  - KDE
    - Kernel function over each sample
    - density=sum of all kernels at x
  - Curse of dimensionality
- Normalising Flows
  - left: X arbitrary data density function
  - right: U parametrised base distribution: standard normal
  - NF: Framework that transforms point of data distribution into point of base distribution
  - vice versa
  - bit more detail
    - transformation is bijective
      - Nfs cannot reduce dimensions
    - f = transforms data towards base distribution
    - g = transforms the other way, inverse, generating
- 1D Transformation
  - left data distribution, Gaussian, variance of 4
    - samples are light blue lines, height indicates density
    - usually this distribution is more complicated and not available
    - just the samples are
  - right: base distribution, standard normal
  - note: area under curve == 1!!
  - how to map the left onto the right and get correct densities?
  - Find a function that turns the left density function into the right one
  - q(x) = p(x)
    - top left, is where we start
    - top right is the goal
    - nothing changed yet
      - too broad
      - must become narrower
  - q(x) = p(x/2)
    - look narrow enough
    - values are too low on Y axis
    - integral is not 1 any more
      - violates a core property of a probability density function
    - how to fix this?
  - q(x) = p(x/2) * 2
    - ‘correct’ the density with factor of 2
  - Two things happened:
    - x was transformed
    - density of transformed x had to be ‘corrected’ with two for some reason
    - lets look at a 2D example to explain why that is and how to deal with it
- Jacobian Matrix and Determinant
  - Lets assume a transformation f, that expands this 1x1 quad into this rectangle
    - here f is constant for all inputs
    - f1 transforms the first dimension of the input, f2 the second
  - how to ‘correct’ the density?
  - Jacobian Matrix
    - matrix of all first derivatives of f regarding all dimensions of it
    - DxD matrix, 2x2 in this case
    - plug in our f, get Jacobian matrix
    - determinant of Jacobian of f(x) is the change of volume of f in x
      - linear approximation in x//
      - 9/2 or 4.5, equals the area of the large base side rectangle
- Now we can formalise the Normalising Flow:
  - a NF models the data distribution, p(x), as the likelihood of the data transformed by f() under a base distribution q()
    - and the correction with the Jacobian determinant we have just seen
  - optimisation target is maximum likelihood
  - Jacobian prevents transformation to collapse all data points into the point of the highest density of the base distribution
  - can build deep models
  - deep models have increased expressiveness
    - can learn more complicated distributions
- Autoregression
  - you may be familiar with autoregression from the time series domain
    - predict t+1 based on time slices up to t
    - this is similar but ‘predicts’ something for dimension d based on the previous dimensions
    - remember: you can remodel any distribution p(x) using the chain rule
      - turns p(x) into a product of conditionals
  - Looking at MADE, Masked Autoencoder for Distribution Estimation, which implements that formula
  - Basically Autoencoder with stripped connections
  - Scheme for a 3D MADE
  - left: input vector, data
  - neural net produces parameters for multivariate Gaussian based on input x
  - multivariate Gaussian used to calculate density of the input x
  - very right: dismantled probability of x, according to the formula
  - wiring:
    - assign IDs from 1..d to input nodes and output nodes, same order
    - assign IDs from 1..d-1 to hidden nodes
    - wire hidden node inputs:
      - only connect nodes with ID <= own
      - first node is not connected to the network
    - wire output nodes:
      - only connect nodes with ID < own
      - second node is not connected to any input
  - How does it work?
    - plug x into the neural net
    - get parameters for multivariate Gaussian
      - no computational path from second dimension to second output
      - one for the third
      - two for the first
      - MADE implements chain rule
    - calculate density
- Masked Autoregressive Flow
  - 1 layer MAF
  - data vector is on the left
  - base distribution: standard normal HERE
  - MADE produces parameters for a transformation based on the input
  - transformation: scales and shifts the input
  - that gives us this U vector
  - p(x) then is the density of that U vector under the base distribution
  - the change of volume is undone by the Jacobian, which is not displayed here
  - autoregression greatly reduces computation time
    - enables to express arbitrary densities
  - 2 layer MAF
    - take the output of MAF1, plug it into MAF2
    - MAF2 permutes order
    - outputs new Us
- Practical Concerns
  - Now the practical part
  - Regarding density estimation
    - find out how close MAFs can get to true, artificial distributions
      - Measure with KL divergence
        - sort of ‘distance’ between the MAF and the true distribution
      - have a look at lower dimensions first
      - look at higher dimensions as well
  - find out how good the generated samples are
    - Measure accuracy of trained classifiers
    - 50 dimensional dataset
- Skipping 1D, since it just fits a Gaussian
- 2D 1G:
  - simplest thing first
  - top left: heatmap of the true density distribution
    - brightness indicates more likelihood
  - other images are divergence maps:
    - red indicates MAF assigns more than the true likelihood
    - blue indicates less
    - bottom right: bar diagram of average KL divergence for each amount of layers
      - a dot is KL of a individual run
    - divergence increases as more layers are added
    - but absolute divergence is low
- 2D 2G
  - show: 1L is insufficient
  - 2 Gaussian bumps
    - Gap between them
  - 1,3,5 and 10 layers
  - divergence is highest for 1L
  - ‘thread’ between two bumps
  - thins out with more layers
  - more layers decreases divergence, 0.018
- 2D 7G
  - show what happens if distribution becomes more complex
  - 7 random Gaussians, not too far apart
  - divergence clearly decreases with more layers added, 0.03
- 2D 4Gc
  - just another, somewhat more complex distribution
  - 4 Gaussians, ‘connected’
  - visually adding more layers seems to reduce divergence
  - look at the average divergence shows that it starts increasing with 10 layers
  - lowest at 5L, 0.012
- 2D 10G
  - show what happens when there large gaps between bumps
  - 10 Gaussian bumps in a larger sample space
  - You can see the threads connecting the bumps
  - divergence decreases with more layers added
  - divergence is high compared to previous examples
  - 0.37, more than 20x as high as the previous one
- 2D KL Overview
  - all experiments
  - brighter means less divergence
  - all scenarios improve with more layers added
    - 4 are worse with 10 then with 5 layers
- 2D Summary
  - generally more layers improve results
  - can have way more layers than dimensions
  - Gaps increase divergence
  - does it hold true for higher dimensions?
- 10D: Results and overview
  - Set of 7 random 10D multivariate Gaussians
  - all experiments share the same set of Gaussians, only their distance is scaled
  - left to right: distance shrinks
    - variance shrinks too
    - mean shrinks until medium
  - 10L not better than 3L
  - either 5L or 7L reach lowest average divergence
  - 20 and 10 layers are the worst
- 10D Summary
  - More layer do not always improve
  - 5 to 7 layers work best
  - layers < dimensions
  - Gaps increase divergence//

- Sampling Quality: MiniBooNE
  - 50 dimensions
  - physical experiment to observe neutrinos
  - binary classification problem of signal and noise
  - ~130k samples, 70% noise
  - Experiment
    - fit one 30 layer MAF for signal, one for noise
    - sample synthetic dataset from MAFs
    - fit multiple classifiers with varying amounts of genuine and synthetic samples
    - measure accuracy on a held out, genuine test set

- MiniBooNE
  - 1
    - a classifier is configured by the amount of genuine and synthetic training samples
    - bottom, horizontal axis: amount of genuine training samples seen by a classifier
      - 0 synthetic samples
    - trained 10 classifiers for each configuration
    - heatmap of average accuracy of 10 classifiers
    - accuracy increases gradually from ~93.8 to 95% when increasing training samples to maximum
    - baseline accuracy is 95%
  - 2
    - lets look at what happens when we switch to synthetic training samples
    - genuine samples are completely replaced by synthetic ones
      - but with same amounts
    - starts at 93.4% and maxes out at 93.7 at 64k samples
    - accuracy drops around 0.4 to 1.5%
    - added colour bar here for reference
  - 3
    - look at the next column, 13k genuine training samples
    - here adding synthetic samples increases the accuracy slightly
    - adding more than ~40k samples is not beneficial anymore
  - 4
    - complete map
    - when more genuine samples are used for training, only adding very few synthetic samples does not worsen the accuracy
    - otherwise there is a gradual decline in accuracy
      - drops from 0.1 to 0.2% when adding the complete synthetic training set

- MiniBooNE balanced ,Accuracy
  - same amount of noise and signal
  - 1
    - using genuine samples only
    - accuracy increases from 93.2 to 94.8%
    - baseline a bit lower
  - 2
    - switching to synthetic samples decreases accuracy by 0.2 to 1%
    - max 93.8%
  - 3
    - adding few synthetic samples improves accuracy by 0.1%
    - adding many reduces it by 0.1 to 0.2%
- MiniBooNE Results
  - Switching to synthetic samples
    - Accuracy drops slightly in all cases
  - Augmenting synthetic samples
    - Complete dataset
      - Does no do anything at best
      - Augmenting many samples is harmful
    - Balanced
      - Few additional samples may improve accuracy very slightly
      - Augmenting many samples is harmful
  - Overall
    - Adding few additional samples to the balanced dataset may improve accuracy a tiny bit
      - personally think it is negligible
- Takeaways
  - MAFs are a great tool that can learn arbitrary distributions
  - MAFs are easy to tune, one big screw: number of layers
  - MAFs scale well for higher dimensions
  - Swiss army knife of density estimation
- The End

- select strftime("%d %m %Y", modified, "unixepoch") as m, path, name from walkfiles where modified < datetime('now') order by m desc;
- select strftime("%d %m %Y", created, "unixepoch") as m, path, name from walkfiles where created < datetime('now') order by m desc;